## Slide 1: Implementation of the Cooley-Tukey Fast Fourier Transform on a 16-bit Microcontroller
Slides by Greg Larmore
Presented on 10/24/12 by Greg Larmore

## Slide 2: About the Presenter
Attends Rose-Hulman Institute of Technology
Bachelor of Science Electrical Engineering – May 2013
Previous experience in low level embedded software and firmware development and code maintenance

## Slide 3: The Fast Fourier Transform (FFT)
Cooley and Tukey reported in 1965 a method for computing Fourier coefficients which required much less computational effort than the traditional discrete Fourier transform (DFT):
Where

## Slide 4: The Cooley-Tukey FFT
This reduction can continue as long as N is divisible by 2.
This method became known as the decimation in time (radix-2) fast Fourier transform
Notes: O(Nlog2(N)) performance instead of O(N^2)

## Slide 5: Decimation in Time FFT Flow Graph
000
000
100
010
110
001
101
111
011
001
010
011
100
101
110
111

## Slide 6: The Hardware
MSP430FR5739 Specifications
16-bit RISC architecture with up to 24MHz clock
16kB FRAM and 1kB SRAM
32-bit hardware multiplier
Ultra-low power operation
  81.4µA/MHz active mode
  6.3µA standby mode
  1.5µA real-time clock
  0.32µA shutdown
MSP-EXP430FR5739 experimenter board

## Slide 7: Firmware Implementation
The firmware to implement the Cooley-Tukey algorithm was written in C++ and uses Q1.15 (signed) fixed point arithmetic accelerated by the 32-bit hardware multiplier.
void FFT(complex<Q1_15> *data, uint8_t inv);
Q1_15& operator*=(const Q1_15 &x) {
//Q1.15 fixed point multiply (hardware)
MPYS = _full;
OP2 = x._full;
_full = RESHI;
return *this;
};

## Slide 8: Firmware Implementation
Twiddle factors for the forward and inverse transforms as well as bit reversal tables are stored as constant arrays based on a predefined length
#if (LENGTH == 4)
const uint16_t BRT[] = {0, 2, 1, 3};
const uint16_t TWIDD[] = {0x7FFF, 0x0000, 0x0000, 0x8000};
const uint16_t INV_TWIDD[] = {0x7FFF, 0x0000, 0x0000, 0x7FFF};
#elif (LENGTH == 8)
const uint16_t BRT[] = {0, 4, 2, 6, 1, 5, 3, 7};
const uint16_t TWIDD[] = {0x7FFF, 0x0000, 0x5A82, 0xA57F, 0x0000, 0x8000, 0xA57F, 0xA57F};
const uint16_t INV_TWIDD[] = {0x7FFF, 0x0000, 0x5A82, 0x5A82, 0x0000, 0x7FFF, 0xA57F, 0x5A82};

## Slide 9: FFT Algorithm Implementation
1 - Bit reverse input
for (i = 0; i < LENGTH; i++) {
j = BRT[i];
if (j < i) {
temp = data[i];
data[i] = data[j];
data[j] = temp;
}
}
2 - Perform radix-2 butterflies
for (i = 0; i < LENGTH; i += 2) {
uint16_t a = i;
uint16_t b = i + 1;
temp = data[a] - data[b];
data[a] += data[b];
data[b] = temp;
}

## Slide 10: FFT Algorithm Implementation
3 - Perform larger butterflies with appropriate twiddle factors
for (n = 2, m = HALF_LENGTH; n < LENGTH; n <<= 1, m >>= 1) {
for (i = 0; i < LENGTH; i += n << 1) {
for (j = 0, k = 0; j < n; j++, k += m) {
uint16_t a = i + j;
uint16_t b = a + n;

## Slide 11: Decimation in Time FFT Flow Graph
000
000
100
010
110
001
101
111
011
001
010
011
100
101
110
111

## Slide 12: FFT Algorithm Implementation
switch (k) {
case 0: //This twiddle is 1 + j0
twidd = data[b];
break;
case HALF_LENGTH: //This twiddle is 0 - j1
twidd.real(data[b].imag());
twidd.imag(-data[b].real());
break;
default:
twidd.real(TWIDD[k]);
twidd.imag(TWIDD[k+1]);
twidd *= data[b];
break;
}
data[b] = data[a] - twidd;
data[a] += twidd;

## Slide 13: FFT Algorithm Implementation
4 - Divide by N for inverse fast Fourier transform
i = HALF_LENGTH;
n = 0;
while (i != 0) {
i >>= 1;
n++;
}
for (i = 0; i < LENGTH; i++) {
data[i].real(Q1_15(data[i].real().full()>>n));
data[i].imag(Q1_15(data[i].imag().full()>>n));
}
DFT
IDFT

## Slide 14: Results
Running at the default 1MHz, 1 FFT was completed in 4,723 cycles when N=8 (4.723ms)
There were some mismatches between the original and the recreated.
These mismatches seem to be due to rounding error from the fixed point arithmetic.

## Slide 15: Conclusions
While the FFT is an effective tool for embedded DSP systems, it is not well suited for a 16-bit microcontroller like the MSP430.
Why?
No floating point arithmetic unit
Insufficient clock speed
Limited memory
16-bit limitation

## Slide 16: Questions?